Airbus A330-300 Pilot's Operating Handbook

Dimensions
Length -	208'11''
Wing Span -	197'9''
Height -	58'0''

Weights (lbs)
Empty Weight -	262,395 lbs
Fuel Weight -	172,768 lbs
Payload -	106,722 lbs
Max.TOW -	520,150 lbs
Max. LW -	407,320 lbs

Powerplants
- A330-303 -	General Electric CF6-80E1 Engines (71,000 lbs thrust)
- A330-323 -	Pratt and Whitney PW4000 Engines (69,000 lbs thrust)
- A330-343 -	Rolls Royce Trent 772B-60 Engines (72,000 lbs thrust)

Operating Performance

- Mno	0.82 Mach Normal Operating Speed
- Mmo	0.86 Mach Max. Operating Speed
- Mne	0.93 Mach Never Exceed Speed
- Vno	330 knots Normal Operating Speed IAS
- Vmo	360 knots Max. Operating Speed IAS
- Vne	380 knots Never Exceed Speed IAS
- Vap	136 – 155 knots (based on total weight) @ Max Flaps/Gears Down
- Vtd	125 – 142 knots (based on total weight)

DO NOT EXCEED 250 KTS AT OR BELOW 10,000 FT ALTITUDE

Take-off Speed @ MTOW

- V1 (Decision Speed) -	140 knots @ Flaps 2 or 3
- VR (Rotation Speed) -	145 knots
- V2 (Safety Speed) -	155 knots

Cruise Speed

- Max Cruise Speed (GS) is 500 kts @ FL300 – FL350 depending on weight
- Typical Cruise Mach is 0.78M – 0.82M @ FL300 – FL350
- Long Range Cruise is 465 kts (GS) @ FL350

ILS & Appraoch Speed @ MLW

- 180 kts Flaps 2 to 136 – 155 knots Full Flaps/Gear Down
- Vapp = 1.3 x Vso (Stall Speed)

Flaps and Gears Extension Speeds

- Flaps 1	240 knots
- Flaps 2 + Slats	215 knots
- Flaps 3 + Slats	196 knots
- Flaps 4 + Gear	186 knots
- Max. Gear Ext.	220 knots

NOTE – The 1+F and 2+F configurations for slats have been removed as in FlightGear, the flaps and slats move together.

Important Cruise Notes

- When flying long routes (over 4hrs) with MTOW, climb to FL300 & hold Alt with cruise speed 0.78 - 0.80 Mach , then fly that level for 30-45 min. then climb to FL310 - 320 @500 fpm and so on until you reach FL350 @ 0.80 - 0.82 Mach.
- Try not exceed 91% N1 during cruise in order to have available thrust for emergencies & be more efficient with fuel burn.

FAA Field Lengths

- Take-off Runway Length	8,700 ft to 9,000 ft
- Landing Runway Length	5,500 ft to 6,000 ft

ETOPS Extended Twin-Engine Operations

If an engine failure occur during cruise forcing an engine shutdown, fly a descend profile on the remaining engine to FL160 (16,000ft) & hold speed between 300 - 420kts. Do not forget to trim to compensate for your lost engine. The A330 can fly the remaining trip on one engine & land @ MLW or lower.

The Airbus A330 is fitted with engines certified ETOPS for 90 , 120 & 180 minutes.

Please checkout the wiki page (http://wiki.flightgear.org/Airbus_A330-200_Series) for more information on the aircraft. Operation Manuals, Checklists and Briefings will be available soon.